## Slide 1: Bilateral Loop Filter in Combination with Sample Adaptive Offset (SAO)
Jacob Ström, Per Wennersten, Jack Enhorn, Du Liu, Kenneth Andersson and Rickard Sjöberg
Ericsson Research

## Slide 2: Background
Transform coding leads to ringing artifacts
transform
quantization
inverse transform
ringing artifacts

## Slide 3: Tools that help with ringing in Versatile Video Coding (VVC)
Sample adaptive offset (SAO): Identifies certain samples using patterns or value range and adds a signaled offset.
Adaptive loop filtering (ALF): Identifies certain samples using gradients and activity and applies a signaled filter.
The idea is to improve this further.
ALF filter support for luma

## Slide 4: Filtering

## Slide 5: Filtering
To filter out noise you want to average over similar samples.

## Slide 6: Filtering
To filter out noise you want to average over similar samples.
In Gaussian filtering the idea is that the closer a sample is, the more it has in common with the sample to be filtered.

## Slide 7: Filtering
To filter out noise you want to average over similar samples.
In Gaussian filtering the idea is that the closer a sample is, the more it has in common with the sample to be filtered.
The weight of a neighbor sample decreases with distance:

## Slide 8: Filtering
original image
After Gaussian filtering
Less noise …
… but blurred
edge.

## Slide 9: Bilateral filtering
original image
same image but where intensity is plotted as the third dimension

## Slide 10: Bilateral filtering
original image
same image but where intensity is plotted as the third dimension

## Slide 11: Filtering
same image but where intensity is plotted as the third dimension
In bilateral filtering the idea is to take the distance both in the spatial domain (distance in pixels) and in the intensity domain (distance in intensity).

## Slide 12: Bilateral filtering
original
Gaussian filter
bilateral filter

## Slide 13: [Wennersten2017]
The version of the filter that was included into the Joint Exploration Model (JEM), which was an exploratory work before VVC.
Bilateral filtering is applied right after reconstruction.
transform coefficients
decoded residual
prediction
clip to [0, 255]
reconstruction
bilateral filter
new
reconstruction
[Wennersten2017] P. Wennersten, J. Ström, Y. Wang, K. Andersson, R. Sjo ̈berg and J. Enhorn, “Bilateral Filtering for Video Coding,” in Proceedings of the IEEE International Conference on Visual Communications and Image Processing (VCIP), Saint Petersburg, FL, USA, Dec. 2017.

## Slide 14: [Wennersten2017]
original
after reconstruction
Strong filtering
removes noise
may remove signal also
Weaker filtering
removes less noise
removes less signal

## Slide 15: [Wennersten2017]
original
after reconstruction
Strong filtering
removes noise
may remove signal also
Weaker filtering
removes less noise
removes less signal
spatial strength
(controlled by block size)
intensity strength (controlled by QP)

## Slide 16: [Wennersten2017]
Was included into JEM
Performance under JEM conformance test conditions in terms of Bjontegaard Delta Rate (BDR)
  All intra: -0.4% BDR 106% encoder run time 105% decoder run time
  Random access: -0.5% BDR 103% encoder run time 100% decoder run time
Drawbacks:
  Needs multiplication
  Limited filter size limits effectiveness
  Is in critical path
This paper addresses these issues

## Slide 17: Addressing drawback #1: Multiplications

## Slide 18: Addressing drawback #1: Multiplications
Using a clever approximation proposed by [Chen2018] the division can be removed:
  where
[Chen2018] Y.-W. Chen et al. “Description of SDR, HDR and 360 video coding technology proposal by Qualcomm and Technicolor low and high complexity versions” in Joint Video Exploration Team (JVET) of ITU-T SG 16 WP 3 and ISO/IEC JTC 1/SC 29/WG 11 10th Meeting, Input document JVET-N0493, San Diego, US, 10-20 Apr 2018

## Slide 19: Addressing drawback #1: Multiplications
Using a clever approximation proposed by [Chen2018] the division can be removed:
  where
  Our proposal: create a 2D look-up table
[Chen2018] Y.-W. Chen et al. “Description of SDR, HDR and 360 video coding technology proposal by Qualcomm and Technicolor low and high complexity versions” in Joint Video Exploration Team (JVET) of ITU-T SG 16 WP 3 and ISO/IEC JTC 1/SC 29/WG 11 10th Meeting, Input document JVET-N0493, San Diego, US, 10-20 Apr 2018

## Slide 20: Addressing drawback #1: Multiplications
Using a clever approximation proposed by [Chen2018] the division can be removed:
  where
  Our proposal: create a 2D look-up table
[Chen2018] Y.-W. Chen et al. “Description of SDR, HDR and 360 video coding technology proposal by Qualcomm and Technicolor low and high complexity versions” in Joint Video Exploration Team (JVET) of ITU-T SG 16 WP 3 and ISO/IEC JTC 1/SC 29/WG 11 10th Meeting, Input document JVET-N0493, San Diego, US, 10-20 Apr 2018

## Slide 21: Addressing drawback #1: Avoiding multiplications
Still have one multiplication

## Slide 22: Addressing drawback #1: Avoiding multiplications
Still have one multiplication
Naïve solution: three-dimensional look-up table. Too expensive.

## Slide 23: Addressing drawback #1: Avoiding multiplications
Still have one multiplication
Naïve solution: three-dimensional look-up table. Too expensive.
Proposed solution: Only allow 3 values of

## Slide 24: Addressing drawback #1: Avoiding multiplications
Still have one multiplication
Naïve solution: three-dimensional look-up table. Too expensive.
Proposed solution: Only allow 3 values of
Bake constant into the LUT: .

## Slide 25: Addressing drawback #1: Avoiding multiplications
Still have one multiplication
Naïve solution: three-dimensional look-up table. Too expensive.
Proposed solution: Only allow 3 values of
Bake constant into the LUT: .
A multiplication with 1, 2 or 3 can be implemented using a single addition in hardware and shift

## Slide 26: Addressing drawback #2: Increasing the filter size
Only one distance to center sample
Two different distances to center sample

## Slide 27: Addressing drawback #2: Increasing the filter size
This would translate to having two look-up tables
  .
  .
Only one distance to center sample
Two different distances to center sample

## Slide 28: Addressing drawback #2: Increasing the filter size
This would translate to having two look-up tables
  .
  .
Instead, we use the same look-up table and just shift by two if it is a diagonal sample:
  Use for diagonal samples
  Use for the regular samples
Only one distance to center sample
Two different distances to center sample

## Slide 29: Addressing drawback #3: Avoiding the critical path
For intra blocks, you need the filtered version of the previous block to get the prediction of the next block
This is a bottleneck in some hardware implementations.
transform coefficients
decoded residual
prediction
clip to [0, 1023]
recon- struction
Before we can predict this block…

## Slide 30: Addressing drawback #3: Avoiding the critical path
For intra blocks, you need the filtered version of the previous block to get the prediction of the next block
This is a bottleneck in some hardware implementations.
transform coefficients
decoded residual
prediction
clip to [0, 1023]
recon- struction
… this block must be finished.
Before we can predict this block…

## Slide 31: Addressing drawback #3: Avoiding the critical path
For intra blocks, you need the filtered version of the previous block to get the prediction of the next block
This is a bottleneck in some hardware implementations.
transform coefficients
decoded residual
prediction
clip to [0, 1023]
recon- struction
bilateral filter
new recon- struction
… this block must be finished.
Before we can predict this block…

## Slide 32: Addressing drawback #3: Avoiding the bottleneck
Instead of filtering each block at the time it is decoded, we wait until all blocks have been decoded

## Slide 33: Avoiding the bottleneck
Instead of filtering each block at the time it is decoded, we wait until all blocks have been decoded
In VVC this is called the loopfilter stage.
Current VVC implementation has three loop-filters:
Deblocking
SAO
ALF
One solution could be to add a fourth loopfilter stage that performs bilateral filtering.
This would solve the bottleneck issue, but to introduce too many loop-filter stages according to HW experts.

## Slide 34: Sharing loop-filter stage with SAO
As can be seen in the figure, the same surrounding samples are used for SAO as for the bilateral filter.

## Slide 35: Sharing loop-filter stage with SAO
Both filter and SAO uses the same samples – SAO does not have to wait for bilateral filter or vice versa.
An implementation can choose to filter bilateral first, SAO first, or in lock-step per sample.
bilateral
SAO
bilateral, clip
SAO, clip

## Slide 36: Results over VTM-6.0
BDR Y Enc run-time Dec run-time
All intra config: -0.40% 106% 104%
Random access config: -0.44% 103% 102%
Low-delay B config: -0.32% 102% 102%
Low-delay P config: -0.39% 103% 102%
LUT: SIMD-friendly (never above 16 bytes long), 60 bytes in total
Two subjective tests were carried out at two JVET meetings
  Gothenburg [JVET-O1118]: Out of 12 examples, one was statistically significant and one almost (confidence interval just touching).
  Geneva [JVET-P1032]: Out of 6 examples, one almost statistically significant (confidence interval just touching).

## Slide 37: Example
VTM6.0
VTM6.0 + bilateral filter

## Slide 38: Example
VTM6.0
VTM6.0 + bilateral filter

## Slide 39: Example
VTM6.0
VTM6.0 + bilateral filter

## Slide 40: Example
VTM6.0
VTM6.0 + bilateral filter

## Slide 41: Example
VTM6.0
VTM6.0 + bilateral filter

## Slide 42: Example
VTM6.0
VTM6.0 + bilateral filter

## Slide 43: Summary
We have described the background and the latest developments for the bilateral filter
Three contributions
  Removal of multiplication
  Increase in filter size
  Combination with SAO to avoid hardware bottleneck

## Slide 44: Thank you!

## Slide 46: Limitations
The encoder must decide what partitioning to use – this is called the RDO process.
A big block may cost fewer bits, but create too much ringing.
However, if this ringing is removed by the bilateral filter in the loop filter stage, it may still be the best option.
Our encoder therefore does bilateral filtering during the RDO process.
This requires an inverse transform in the encoder, which is expensive.
or
?

## Slide 47: Example
VTM6.0
VTM6.0 + bilateral filter with RDO optimization
VTM6.0 + bilateral filter without RDO optimization

## Slide 48: Results over VTM-5.0
BDR Y Enc run-time Dec run-time
All intra config: -0.40% 106% 104%
Random access config: -0.50% 102% 102%
Low-delay B config: -0.31% 103% 104%
LUT: SIMD-friendly (never above 16 bytes long), 60 bytes in total
Two subjective tests were carried out at two JVET meetings
  Gothenburg [JVET-O1118]: Out of 12 examples, one was statistically significant and one almost (confidence interval just touching).
  Geneva [JVET-P1032]: Out of 6 examples, one almost statistically significant (confidence interval just touching).

## Slide 49: Outline
What we try to accomplish
How bilateral filters work
Previous work in detail
The contribution of this paper

## Slide 50: Gaussian filtering
Weights depend on squared distance to center of filter.
1
1
d

## Slide 51: Gaussian filtering
Weights depend on squared distance to center of filter.
If we get
Example
1
1
d

## Slide 52: Gaussian filtering
Weights depend on squared distance to center of filter.
If we get
Normalizing filter coefficients to 1:
Example
1
1
d

## Slide 53: Gaussian filtering
Weights depend on squared distance to center of filter.
If we get
Normalizing filter coefficients to 1:
After normalizing we get
Example
1
1
d

## Slide 54: Gaussian Filtering blurs edges
3x3 Gaussian filter
Less noise …
… but blurred edge.

## Slide 55: Gaussian filtering blurs edges
Even with a small weight such as , its contribution is large enough to be visible
Middle pixel will brighten by 64 intensity steps.

## Slide 56: Bilateral filtering
The weights depend on the squared distance to the center of the filter and the intensity difference
1
1
d

## Slide 57: Bilateral filtering
The weights depend on the squared distance to the center of the filter and the intensity difference
Normalizing filter coefficients to 1:
If we get
After normalizing we get
Example
1
1
d

## Slide 58: [Wennersten2017]
original
after reconstruction
Strong filtering
removes noise
may remove signal also
Weaker filtering
removes less noise
removes less signal

## Slide 59: [Wennersten2017]
Filter strength set on heuristics in Wennersten2017
Higher QP -> larger compression artifacts -> stronger filtering better
  Set intensity strength as a function of QP:
Smaller blocks -> sharp edges -> more ringing -> stronger filtering better
  Set spatial strength as a function of transform block size:
spatial strength
intensity strength

## Slide 60: Drawbacks with [Wennersten2017]
Weights are different for every sample, since is different

## Slide 61: Drawbacks with [Wennersten2017]
Weights are different for every sample, since is different
This means that the normalizing denominator will be different
different every sample

## Slide 62: Drawbacks with [Wennersten2017]
Weights are different for every sample, since is different
This means that the normalizing denominator will be different
A division per pixel is necessary. ([Wennersten2017] used a division table)
different every sample

## Slide 63: Drawbacks with [Wennersten2017]
Weights are different for every sample, since is different
This means that the normalizing denominator will be different
A division per pixel is necessary. ([Wennersten2017] used a division table)
This was addressed by [Chen2018]:
  They use in numerator, but
  in denominator
different every sample

## Slide 64: Drawbacks with [Wennersten2017]
Weights are different for every sample, since is different
This means that the normalizing denominator will be different
A division per pixel is necessary. ([Wennersten2017] used a division table)
This was addressed by [Chen2018]:
  They use in numerator, but
  in denominator
different every sample
sum same every sample – change to multiplication with

## Slide 65: Drawbacks with [Wennersten2017]
Small filter size
  Only 4-neighbors used
  Can only cancel high frequency ringing
Multiplications needed:

## Slide 66: Contributions of this paper
A way to combine the filter with SAO to avoid the prediction bottleneck
An increase in filter size
A simplification of the filter that avoids multiplications

## Slide 67: Addressing drawback #1: Increasing the filter size
Increasing the filter size makes it possible to remove more types of ringing.

## Slide 68: Problem of having too many loopfilter stages
Simplest implementation is to filter entire image before starting with next:
  Deblock entire image, and then
  Perform SAO on entire image, and then,
  Perform ALF on entire image
To reduce latency, many implementations filter in parallel, for instance
  Deblock top quarter, and then
  Perform SAO on top quarter while deblocking second quarter, and then
  Perform ALF on top quarter, SAO on second quarter and deblocking on third
A problem occurs if one stage takes longer than normal – then the next stages cannot start because of has not gotten the data yet (data starvation)
Creating one new loopfilter stage makes this situation even worse

## Slide 69: Problem of having too many loopfilter stages
Simplest implementation is to filter entire image before starting with next:
  Deblock entire image, and then
  Perform SAO on entire image, and then,
  Perform ALF on entire image
To reduce latency, many implementations filter in parallel, for instance
  Deblock top quarter, and then
  Perform SAO on top quarter while deblocking second quarter, and then
  Perform ALF on top quarter, SAO on second quarter and deblocking on third
A problem occurs if one stage takes longer than normal – then the next stages cannot start because of has not gotten the data yet (data starvation)
Creating one new loopfilter stage makes this situation even worse
deblock

## Slide 70: Problem of having too many loopfilter stages
Simplest implementation is to filter entire image before starting with next:
  Deblock entire image, and then
  Perform SAO on entire image, and then,
  Perform ALF on entire image
To reduce latency, many implementations filter in parallel, for instance
  Deblock top quarter, and then
  Perform SAO on top quarter while deblocking second quarter, and then
  Perform ALF on top quarter, SAO on second quarter and deblocking on third
A problem occurs if one stage takes longer than normal – then the next stages cannot start because of has not gotten the data yet (data starvation)
Creating one new loopfilter stage makes this situation even worse
deblock
SAO

## Slide 71: Problem of having too many loopfilter stages
Simplest implementation is to filter entire image before starting with next:
  Deblock entire image, and then
  Perform SAO on entire image, and then,
  Perform ALF on entire image
To reduce latency, many implementations filter in parallel, for instance
  Deblock top quarter, and then
  Perform SAO on top quarter while deblocking second quarter, and then
  Perform ALF on top quarter, SAO on second quarter and deblocking on third
A problem occurs if one stage takes longer than normal – then the next stages cannot start because of has not gotten the data yet (data starvation)
Creating one new loopfilter stage makes this situation even worse
deblock
ALF
SAO

## Slide 72: Problem of having too many loopfilter stages
Simplest implementation is to filter entire image before starting with next:
  Deblock entire image, and then
  Perform SAO on entire image, and then,
  Perform ALF on entire image
To reduce latency, many implementations filter in parallel, for instance
  Deblock top quarter, and then
  Perform SAO on top quarter while deblocking second quarter, and then
  Perform ALF on top quarter, SAO on second quarter and deblocking on third
A problem occurs if one stage takes longer than normal – then the next stages cannot start because of has not gotten the data yet (data starvation)
Creating one new loopfilter stage makes this situation even worse
SAO
ALF
deblock

## Slide 73: Problem of having too many loopfilter stages
Simplest implementation is to filter entire image before starting with next:
  Deblock entire image, and then
  Perform SAO on entire image, and then,
  Perform ALF on entire image
To reduce latency, many implementations filter in parallel, for instance
  Deblock top quarter, and then
  Perform SAO on top quarter while deblocking second quarter, and then
  Perform ALF on top quarter, SAO on second quarter and deblocking on third
A problem occurs if one stage takes longer than normal – then the next stages cannot start because of has not gotten the data yet (data starvation)
Creating one new loopfilter stage makes this situation even worse
ALF
SAO

## Slide 74: Problem of having too many loopfilter stages
Simplest implementation is to filter entire image before starting with next:
  Deblock entire image, and then
  Perform SAO on entire image, and then,
  Perform ALF on entire image
To reduce latency, many implementations filter in parallel, for instance
  Deblock top quarter, and then
  Perform SAO on top quarter while deblocking second quarter, and then
  Perform ALF on top quarter, SAO on second quarter and deblocking on third
A problem occurs if one stage takes longer than normal – then the next stages cannot start because of has not gotten the data yet (data starvation)
Creating one new loopfilter stage makes this situation even worse
ALF

## Slide 75: Problem of having too many loopfilter stages
Simplest implementation is to filter entire image before starting with next:
  Deblock entire image, and then
  Perform SAO on entire image, and then,
  Perform ALF on entire image
To reduce latency, many implementations filter in parallel, for instance
  Deblock top quarter, and then
  Perform SAO on top quarter while deblocking second quarter, and then
  Perform ALF on top quarter, SAO on second quarter and deblocking on third
A problem occurs if one stage takes longer than normal – then the next stages cannot start because of has not gotten the data yet (data starvation)
Creating one new loopfilter stage makes this situation even worse